# Toyota Differential ID Codes

| First Digit |  | Second & Third Digits |
| --- | --- | --- |
| Diameter of | Code |  | Gear Ratio | Code |  | Gear Ratio | Code |  | Gear Ratio | Code |
| Ringgear |  |  |  |  |  |  |  |  |  |  |
| 138mm | A |  | 3.300 | 01 |  | 3.364 | 27 |  | 3.356 | 48 |
| 145mm | B |  | 3.360 | 02 |  | 4.300 | 28 |  | 3.729 | 49 |
| 6.25" | C |  | 3.545 | 03 |  | 4.100 | 29 |  | 3.400 | 50 |
| 6.62" | D |  | 3.556 | 04 |  | 3.727 | 30 |  | 3.736 | 51 |
| 7.1" | E |  | 3.700 | 05 |  | 3.909 | 31 |  | 3.722 | 52 |
| 7.5" | F |  | 3.889 | 06 |  | 6.591 | 32 |  | 3.250 | 53 |
| 8" | G |  | 3.900 | 07 |  | 4.807 | " |  | 3.941 | 54 |
| 9" | H |  | 4.111 | 08 |  | 7.503 | 33 |  | 3.333 | 55 |
| 9.25" | J |  | 4.222 | 09 |  | 5.583 | " |  | 2.821 | 56 |
| 9.5" | K |  | 4.375 | 10 |  | 6.781 | 34 |  | 4.058 | 57 |
| 10.5" | L |  | 4.444 | 11 |  | 4.786 | " |  | 3.238 | 58 |
| 12.5" | M |  | 4.625 | 12 |  | 7.636 | 35 |  | 3.234 | 59 |
| 13.5" | N |  | 4.790 | 13 |  | 5.600 | " |  | 3.519 | 60 |
| 14" | P |  | 4.875 | 14 |  | 4.778 | 36 |  | 2.724 | 61 |
| 12" | Q |  | 5.125 | 15 |  | 3.583 | 37 |  | 2.892 | 62 |
| 162mm | R |  | 5.286 | 16 |  | 3.417 | 38 |  | 2.655 | 63 |
| 6.38" | S |  | 5.600 | 17 |  | 3.154 | 39 |  | 4.312 | 64 |
| 6.7" | T |  | 5.714 | 18 |  | 5.375 | 40 |  | 3.837 | 65 |
| 6" | U |  | 5.833 | 19 |  | 3.308 | 41 |  | 3.071 | 66 |
| 10.6" | V |  | 6.167 | 20 |  | 6.500 | 42 |  | 3.526 | 67 |
| 15.5" | W |  | 6.667 | 21 |  | 3.550 | 43 |  | 3.095 | 68 |
| 142mm | X |  | 6.780 | 22 |  | 3.214 | 44 |  | 4.176 | 69 |
| 158mm | Y |  | 6.833 | 23 |  | 3.533 | 45 |  | 5.857 | 70 |
| 202mm | Z |  | 7.640 | 24 |  | 2.928 | 46 |  | 2.962 | 71 |
| no ringgear | - |  | 4.556 | 25 |  | 2.929 | " |  | 3.949 | 72 |
|  |  |  | 5.571 | 26 |  | 3.944 | 47 |  | 4.285 | 73 |
| Fourth Digit |  |  |  |  |  |  |  |  |
| Number of | Code | Limited Slip |  |  |  |  |  |  |  |  |
| Pinions |  |  | ..meaning |
| 2 | 2 | NO | T312 = 6.7" Ringgear, 3.909 Ratio and 2 spider NO LSD |
| 2 | 3 | YES | G295 = 8" Ringgear, 4.100 ratio and 4 spider LSD. |
| 4 | 4 | NO | -474 = NO ringgear (FWD) 3.944 Ratio and 4 spider NO LSD |
| 4 | 5 | YES | P194 = someone just sold you a truck diff…..OOOPS! |

Special Thanks to Roadrunner for allowing me to reproduce this Information.